## Slide 2: Edible Oil Industry
Technology Challenges and Solutions
Bent Sarup
2007 ICFMCE
Dubai
November 25, 2017

## Slide 3: Outline
Industry overview and trends
Technology introduction
Examples of new developments
Summary

## Slide 4: Oil demand has been on a steady growth path
Ref. Oil World, Sep 23, 2016

## Slide 5: Biofuel demand foreseen to reduce
Reference: OECD-FAO AGRICULTURALOUTLOOK (2017)

## Slide 6: Consumption per Capita CAGR 2010-2015 = 3.5%
Reference:
Annex A, OECD-FAO AGRICULTURALOUTLOOK (2015)
The most developed countries consume about twice the amount of oil per capita (but stagnating) as an average developing country (growing)

## Slide 7: Edible Oil Industry Overview
Crude Oil
- palm
- soybean
- rapeseed
- sunflower
- corn
- coconut
- palm kernel
- cottonseed
- groundnut
- ricebran
- tallow
- fish
Refining
Liquid edible oils
Pretreatment +
transesterification
Fat modification
Biodiesel
Specialty fats
Fat splitting,
distillation, ..
Glycerin
Fatty acids
Oleochemicals
EXTRACTION

## Slide 8: Edible oil industry drivers
Solid structural growth (food demand)
Healthier foods (nutritional value, safety)
Minimize losses and utilize byproducts
Energy efficiency
Sustainability
www.alfalaval.com

## Slide 9: Edible Oil Refining

## Slide 10: R&D in process system development
Customer
Universities
Sub-suppliers
Process solution supplier
Funding agencies
Time
Performance

## Slide 11: Example 1. University collaboration
Modelling of lipid systems and application example for micronutrient recovery

## Slide 12: Challenges in lipid modelling
Experimental measurements for obtaining properties of lipids of interest are time consuming, expensive, sometimes may not even be feasible.
Issues related to accuracy and reliability of the available data and property prediction models need particular attention.
Design & analysis of lipids processes require:
  databases containing necessary property information
  reliable and consistent property prediction models
  validation of data & property models using reliable plant data

## Slide 13: Some lipid molecular structures
A triglyceride
A free fatty acid
Β-tocopherol
Β-sitosterol
http://upload.wikimedia.org/wikipedia/commons
A phospholipid

## Slide 14: Property prediction by GC methods
For Primary Properties of Lipids
For Temperature Dependent Properties of Lipids
Marrero and Gani group-contribution (GC) Method 1
The function f (X) is a function contains the target property X.
Atom Connectivity Index Method 2
(is used to create/predict missing group contributions)
Quantification of confidence intervals 3
(to assess reliability of the predictions)
Ceriani et al. (2012) GC Method 4
(for prediction of vapor pressure and heat of vaporization
of lipids)
REFERENCES:
1 J. Marrero, and R. Gani, Fluid Phase Equilibria, (2001), 183-208.
2 R. Gani et al. Industrial and Engineering Chemistry Research, (2005), 7262-7269.
3 A. Hukkerikar et al., Fluid Phase Equilibria, 321 (2012) 25-43.
4 R. Ceriani, R. Gani, Y. A. Liu, Fluid Phase Equilibria, (2012), 53-59.

## Slide 15: SPEED Lipids Database. Structure & Features
“Thermodynamic needs for the oleochemical industries”, Bent Sarup,
Olivia A. Perederic, Sawitree Kalakul, John M. Woodley, Rafiqul Gani, 16th AIChE Meeting (2016)
Notes: Database (db) organized in 2 parts, both containing experimental data and property models
Database is connected to Lipids Toolbox which has different features: db search, property models regression, consistency check, database management witch allows the db connection with process and product simulator.
Check presentation – more details on the database

## Slide 16: SPEED Lipids Database. Models performances
  330 compounds
  24 property models
Pure Compounds
Pure compounds properties consistency check
NBP
Diglycerides
Monoglycerides
“Thermodynamic needs for the oleochemical industries”, Bent Sarup,
Olivia A. Perederic, Sawitree Kalakul, John M. Woodley, Rafiqul Gani, 16th AIChE Meeting (2016)
Triglycerides
Notes: Pure compounds part contains info on 330 compounds for 24 property models (primary and temperature dependent).
DAG: no experimental data, MAG experimental data just for 1 compound

## Slide 17: Micronutrient recovery
Deodorizer distillates contain a number of valuable components such as tocopherols, tocotrienols, sterols and squalene, sometimes referred to as volatile “micronutrients”
However, low recovery from the deodorized oil and their concentration in the deodorizer distillates limits the feasibility of further processing of these distillates in dedicated facilities for separation and purification of the micronutrients
It is therefore of considerable interest to improve the understanding of design and operating variables that increase the feasibility of micronutrient utilisation

## Slide 18: Recovering micronutrients ”Double scrubber”

## Slide 19: Process simulation example
Oil Soybean oil
Column: Packed (structured packing)
Operating conditions 260 ºC, 0.75% sparge steam, 2.5 mbar vacuum
Oil composition
Simulation model PRO/II with in-house lipid property data base

## Slide 20: Tocopherols in the hot destillate

## Slide 21: ”Double Scrubber” Main Characteristics
© Alfa Laval
Slide 21
Optimum operation requires compromising of tocopherol yield and concentration
Relatively narrow range of optimum hot scrubber temperatures
Only stripping and condensation, no rectification functionality
Notes: © Alfa Laval
21

## Slide 22: Alfa Laval TocoBoost®
Patents granted and pending (e.g. EP 2597142)

## Slide 23: Loss of Toco’s in FFA Product
© Alfa Laval
Slide 23
Patents granted and pending (e.g. EP 2597142)
TocoBoost®
Double scrubber
Notes: © Alfa Laval
23

## Slide 24: Example 2. Supplier collaboration
Enzymatic degumming

## Slide 25: Gum content in crude oils

## Slide 26: Hydration rates of phosphatides

## Slide 27: Phospholipids cause oil loss

## Slide 28: Enzymes reduce degumming yield loss

## Slide 29: Enzymatic deep degumming process

## Slide 30: Enzymatic refining of water degummed oil
Advantages
  no soapstock
  no wash water
  robust
By-products
  lyso-gums
  FFA
 | Caustic refining | Enzymatic refining
P level in oil | 150 ppm | 150 ppm
P level after centrifuge | 2 ppm | 2 ppm
Soapstock (%) | 1.51 | 0
Dry lyso gums (%) | 0 | 0.5
Refining loss (%) | 1.42 | 0.45
Ref :Dayton, C., Nov. 2005 Germany

## Slide 31: Physical refining plant, enzymatic degumming

## Slide 32: Summary
The fats and oils industry is of key importance for food supply as well as a sustainable source of chemicals and liquid fuel.
Technology for the industry continues to undergo change to develop efficiency, minimize losses and provide healthier end products.
A broad collaboration between the customers, edible oil technology suppliers, universities and suppliers is essential to gain speed in process system development.