## Slide 2
Flavio Manenti
CMIC Dept. “Giulia Natta”
Centre for Sustainable Process Engineering Research (SuPER)
AG2S™ technology: the new route for effective CO2 reuse
Dubai, November the 25th 2017, Keynote Lecture, at:
ICFMCE – International Conference on Functional Materials and Chemical Engineering

## Slide 3: CO2 reuse – Motivation
CO2 as feedstock Established processes
Anthropogenic CO2 emissions:
about 33 Gt/y[1]
[1] Le Quéré et al., Earth System Science Data Discussions, 2012, 2015.
CO2 as feedstock, today Where and how much?

## Slide 4: Urea plant
Main use: fertilizer
Plant: large size, downstream the ammonia plant
  Toyo, Casale, Uhde, Stamicarbon, Eni…
Synthesis: 2 NH3 + CO2  (NH2)2CO + H2O
Ref.: http://www.unido.or.jp/en/technology_db/428/
Ref.: https://www.mhi-global.com/products/expand/km-cdr_application_03.html
Worldwide CO2 reuse in urea plants: 187 Mt[1]
[1] Ceresana, Market Study Urea, 2016. ceresana.com

## Slide 5: Methanol plant
Main uses: energy carrier, fuel, base chemical
Perspectives: methanol economy[1]
Plant: large size, downstream the syngas production
  Lurgi, Davy, Toyo, Casale, Air Products, Topsoe…[2]
Synthesis CO + 2 H2  CH3OH; CO2 + 3 H2  CH3OH + H2O; WGS
[1] Olah, G. A. (2005). "Beyond Oil and Gas: The Methanol Economy." Angewandte Chemie International Edition 44(18): 2636-2639.
[2] Bozzano, G., Manenti F. (2016). Efficient Methanol synthesis: Perspectives, Technologies and Optimization Strategies, Progress in Energy and Combustion Science, 56, 71–105
Worldwide CO2 reuse in MeOH plants: 58 Mt[3]
[3] Petroleum Economist, 2016, petroleum-economist.com

## Slide 6: Other technologies
Dry reforming
  Pilot-scale
  Synthesis [1]
    CH4 + CO2  2 CO + 2 H2
Sabatier process
  Pilot-scale
  Peak-to-gas
  Synthesis [2]
    CO2 + 4 H2  CH4 + 2 H2O
GTL
  Demo-scale, few large-scale
  Synthesis [3]
    CO + 2 H2  -[CH2]- + H2O
    Water Gas Shift (WGS)
[1] Pakhare, D., Spivey, J. (2014), A review of dry (CO2) reforming of methane over noble metal catalysts, Chemical Society Reviews, 43(22), 7813-7837
[2] Che, M., Nobel Prize in chemistry 1912 to Sabatier: Organic chemistry or catalysis? Catalysis Today, 218–219, 162-171, 2013
[3] Pirola, C. et al., Fischer–Tropsch synthesis: EXAFS study of Ru and Pt bimetallic Co based catalysts, Fuel, 132 (2014) 62–70
Current worldwide CO2 reuse is negligible

## Slide 7
What else?
H2 availability is the key point…
H2 sources?

## Slide 8: Hydrogen (large-scale) production
Industrial scale
  Source:
    methane, naphtha
    steam methane reforming
  Source:
    coal, biomass, urban waste
    gasification
Other proposed molecules
  CH3OH, NH3
  H2O (Power-to-gas)
Renewables
To reuse on-site the CO2 in the process industry (looping)
We need hydrogen or hydrogen-rich molecules
We need energy

## Slide 9
CH4, CH3OH, NH3, H2O…
… and H2S?
A natural and synthetic compound

## Slide 10: H2S processing today
Claus process:
Comb Air
Acid Gas
SWS
MP Steam
LP Steam
Stack / TG
Sulfur
Thermal Reactor
WHB
Cond. 1-2
Claus 2
Claus 1
Cond. 3
Water
    H2S + 1.5 O2  SO2 + H2O
    2 H2S + SO2  1.5 S2 + 2 H2O

## Slide 11: New: Acid gas to Syngas™ technology
New technology (Regenerative Thermal Reactor)
  Overall reaction: 2 H2S + CO2  CO + H2 + S2 + H2O
  3 moles of emissions into 2 moles of syngas
  Energy self-sustainability (minor O2 injection)
Regenerative sect.
Recuperative sect.
H2S
CO2
Raw Syngas
Water
Steam
H2S
(Acid gas)
CO2
O2 (or air)
Effluent
(>1000°C)
Pre-heated Recycle
H2S, CO2
Manenti et al., Granted patent WO 2015/015457 A1

## Slide 12: Regenerative Thermal Reactor (RTR)
Main effects using RTR[1]
  Good CO2 and H2S conversion
  Handling impurities
  Inhibition of side-reactions
Regenerative sect.
Recuperative sect.
H2S
CO2
Raw Syngas
Water
Steam
H2S
(Acid gas)
CO2
O2 (or air)
Effluent
(>1000°C)
Pre-heated Recycle
H2S, CO2
[1] Manenti et al., Syngas from H2S and CO2: an Alternative, Pioneering Synthesis Route?, Hydrocarbon Processing, 38-41, June 2016

## Slide 13
Defeating CO2 thermal stability H2S main role

## Slide 14: Reducing radicalic pool

## Slide 15
Process scale Technology layout

## Slide 16: AG2S™ complete layout
  2 H2S + CO2  CO + H2 + S2 + H2O
  COS + H2O  CO2 + H2S
  CS2 + 2 H2O  CO2 + 2 H2S
  CO + H2O  CO2 + H2
  2 H2S + SO2  1.5 S2 + 2 H2O

## Slide 17: Main benefits and potential
Complete conversion of H2S (as per Claus process)
Cut of CO2 emissions
Reduced use of air or O2
Production of syngas from two wastes
Exploitation of sulfur-rich resources
  Sulfur-rich coal, shale, oil; H2S-rich streams of NG, shale gas
  Currently unexploited sources
Production of commodities using CO2 as feedstock
  Perspective: main process for CO2 reuse
Reduced investment for revamping
CO2-free synthesis of base chemicals ( )
  Methanol, (synthetic) fuels, olefins, polymers…
Based on worldwide sulfur production, current potential of AG2S™ is about 44 Mt/y of syngas
Perspective: debottlenecking sulfur-rich sources, AG2S™ potential appears much higher

## Slide 18
A case study Coal gasification

## Slide 19: Coal gasification[1]
Use: syngas production
Plant
  large size
  CTX plants
Synthesis
  C + H2O  CO + H2
Energy supply
  In situ
  C + O2  CO2
[1] Bassani, A., Acid Gas to Syngas (AG2S™) technology applied to solid fuel gasification: Cutting H2S and CO2 emissions by improving syngas production, Applied Energy, 2016, doi:10.1016/j.apenergy.2016.06.040

## Slide 20: Tools & pilots
Pilots at Sotacarbo facilities
GasDS suite[1] & AspenHysys-PRO/II
GasDS suite
    Chemical kinetics
      Torrefaction, pyrolysis, gasification, combustion
    Reactor configurations
      Updraft, Downdraft, Traveling grate, Fluidized, …
    Design & operational purposes
      Support, Optimization, Validation, Dynamics
      Monitoring, Prediction, Control, Start-up assistant
[1] Ranzi, E., Faravelli, T., Manenti, F., Pyrolysis, Gasification, and Combustion of Solid Fuels, Advances in Chemical Engineering, Elsevier, ISSN 0065-2377, 1-94, 2016.

## Slide 21: Techno-economic study
Input:
  Coal with 5%w sulfur
  Coal gasifier: 77 t/h
Revamp
  Gas/gas heat exchanger
    49700 kg, 727 k$
  Burner
    165 k$
  Amine washing
    New unit (in spare)
    30 m3/h, 6.16 M$
Payback: 1.63y
  Accounting for syngas only
    Not considered: CO2 certificates, sulfur, sulfur-rich resources

## Slide 22
Technology potential Application areas

## Slide 23: Potential application areas
CO
Formylation
Carbonylation
Metals
Metal carbonyls
Acetic acid
Superconductors
Sulfur
Sulfuric acid
Claus
Hydrodesulfurization
Coal
Coal gasification
Coke oven gas
Shale
Shale oil
Shale gas
Oil&gas
Natural gas
Crude oil
Heavy oil
Renewables
Biomass/biogas
Geothermal
Hydrogen
Power generation
Hydrotreating
Gasification
Reforming
Fuel
…
Syngas
Ammonia
Synthetic fuels (GTL)
Methanol/DME
Acetic acid
Superior alcohols/ethers/acids

## Slide 24: Natural gas field
Let-down
Natural gas with 20%v H2S content
Liquid streams
Sweetening
Acid gas compression and injection
Total gas streams
100%v
Gas field
20%v
40%v
Energy
10%v
30%v
40%v
H2S, CO2
H2S, CO2
40%v

## Slide 25: Natural gas field
Let-down
Natural gas with 20%v H2S content
Liquid streams
Sweetening
Acid gas compression and injection
Total gas streams
100%v
AG2S™ technology
AG2S™ IS HIGHER-PERFROMANCE GAS FIELD
Gas field
20%v
40%v
Energy
10%v
30%v
40%v
H2S, CO2
H2S, CO2
52%v
40%v
Sulfur, water
15%v
10%v
CO2
3%v
10%v
CO2
More gas production
Less energy consumption
Longer drill life (no H2S re-injection)

## Slide 26: Oil shale
Retorting
Refining
Products
100%v
Oil shale deposit
Energy
Exhaust oil shale
70%v
Raw oil shale
20%v
By-products
5%v
5%v
(acid gases)

## Slide 27: Oil shale
Retorting
Refining
Products
100%v
AG2S™ technology
Oil shale deposit
Energy
Exhaust oil shale
70%v
Sulfur
Water
5%v
70%v
25%v
Raw oil shale
20%v
By-products
5%v
5%v
65%v
5%v
(acid gases)
AG2S™ IS SHALE OIL BOOSTER
Reduced environmental impact
Higher production yield
Better shale exploitation
Portability
Compact, portable module

## Slide 28: Oil refining – HDS/Reforming
Steam reforming
Steam
Naphtha
WGSR
HDS
H2
100%v
400%v
15%v
100%v
Combustion air
150%v
Flue gases
165%v
PSA
CO2
100%v
H2S
400%v
Oil with sulfur
Oil

## Slide 29: Oil refining – HDS/Reforming
Steam reforming
Steam
Naphtha
WGSR
HDS
H2
100%v
AG2S™ technology
400%v
15%v
200%v
AG2S™ IS HYDROGEN RECOVERY
Less flue gas/CO2 environmental impact
Internal hydrogen loop
Reduced reforming duty
Better naphtha potential exploitation
100%v
Combution air
150%v
Flue gases
165%v
PSA
CO2
100%v
H2S
400%v
Oil with sulfur
Oil
H2, CO
50%v
50%v
8%v
80%v
88%v
50%v
Sulfur, water
200%v

## Slide 30: CO2-free coal-to-methanol process
Coal gasifier
Coal with 20% sulfur content
Steam
O2 or air
Ash
Dewatering
Sweetening
H2O
H2S, CO2
MeOH
100%v
40%v
60%v
Synthesis

## Slide 31: CO2-free coal-to-methanol process
Coal gasifier
Coal with 20% sulfur content
Steam
O2 or air
Ash
Dewatering
Sweetening
H2O
H2S, CO2
MeOH
100%v
40%v
60%v
Synthesis
AG2S™ technology
Market sulfur
Water
Remaining CO2
MeOH surplus
20%v
10%v
10%v
AG2S™ IS GREENER COAL USES
Less (no) CO2 environmental impact
More syngas production
Less coal uses with same production
Better coal potential exploitation

## Slide 32: Conclusions
We are preventing CO2 formation
Thanks to renewables
We are capturing CO2 by pre-/post-combustion CCS technologies
We are not yet reusing CO2 as in our possibilities
Just less than 1% is currently reused
AG2S™ will allow to cut reuse several percents
After H2020, a large program on CO2 reuse (CCU) will be launched in EC
Atmospheric CO2 / emissions will unavoidably be the future carbon source for chemistry, chemical & process engineering

## Slide 33: Acknowledgements

## Slide 34
Flavio Manenti Professor of Chemical Plants and Operations Executive Board of EFCE, AIDIC, CAPE-WP, AIAC POLITECNICO DI MILANO Dipartimento di Chimica, Materiali e Ingegneria Chimica "G. Natta" Sustainable Process Engineering Research (SuPER) team Piazza Leonardo da Vinci, 32, 20133 Milano, ITALY TECHNISCHE UNIVERSITAT BERLIN Alexander von Humboldt Professor DBTA (Dynamic und Betrieb Technischer Anlagen) Faculty Sekt. KWT 9, Strasse des 17.Juni, 135 - D-10623 Berlin, GERMANY (Mobile) +39.338.5665817 (Phone) +39.(0)2.2399.3273 - +49.(0)30.314.23418 (Email) flavio.manenti@polimi.it WELCOME… - (Web) http://super.chem.polimi.it
Thanks for the kind attention

## Slide 35
Flavio Manenti, flavio.manenti@polimi.it