## Slide 1: Applications of Reverse Osmosis for the Removal of Organic Compounds from Wastewater: Modelling and Simulation I. M. Mujtaba, M. A. Al-Obaidi, C. Kara-Zaïtri Chemical Engineering, Faculty of Engineering and Informatics University of Bradford. Bradford
ICFMCE 2017 – 24-26 November 2017, Dubai

## Slide 2
Bradford Chemical Engineering
4th in the UK
Guardian League Table, 2018

## Slide 5: Presentation Outline
A. Introduction
Water and water scarcity
Wastewater and associated challenges
B. Wastewater Treatment Methods
Reverse osmosis process
The feasibility of the RO process for wastewater
The RO process modelling
Distributed Modelling of the Spiral Wound RO Process
The Model of Al-Obaidi et al. [16]
The Model of Al-Obaidi et al. [17]
C. Results/Discussions/Conclusions

## Slide 6: A. Introduction
Water and water scarcity
Increasing demand for freshwater due to population growth and increasing standard of living
Water shortage will lead to further development and implementation of technologies for water reclamation and reuse.
Huge volumes of wastewater including sewage and industrial effluents are disposed off into rivers and oceans (damaging the marine environment).

## Slide 7: A. Introduction: Wastewater Challenges
A wide variety of the complex toxicological compounds which adversely affect the natural ecosystem and human health
The organic pollutants found in wastewater can neither be easily nor cheaply removed.
Wastewater treatment is a much more difficult process than water desalination
https://www.slideshare.net/Mominu/water-pollution-in-bangladesh-43331625
http://banglaroot.org/environment/

## Slide 8
Reclaimed Water Applications
Industrial reuse: Reclaimed water of low quality is utilised in cooling towers and power plants due to high-water demand.
Agricultural and irrigation: These are considered as the highest consumers of recycled water for irrigating edible and non-edible agricultural crops. This is due to low cost of wastewater with nutrient content that eliminates the use of fertilizers.
As potable water: Singapore.

## Slide 9
Reclaimed Water Applications
Table 1: Purposes and rates of using wastewater in some countries [1].
Country | Purpose | Rate | Notes
Pakistan | Agricultural | 96% | Non-treated wastewater
Tunisia | Agricultural | 86% | Treated wastewater
Namibia | Municipal | 29% | Namibia and Singapore have the most important water reuse for human consumption reclamation projects
Singapore | Municipal | 45% | 
 | Industrial | 51% | 
USA | Industrial | 45% | USA and Germany have a larger number of recycling and reuse projects across various industries
Germany | Industrial | 69% | 

## Slide 10
High toxicity even at low concentrations
Oral tolerable daily intake of phenols is ~ 0.5 mg/kg/day
The WHO has set the phenol concentration to 1 µg/l in drinking water
The existence of a stable benzene ring in phenol and phenolic derivatives has increased their resistance to biological decomposition
Can be found in in wastewater effluents of :
Refineries (6-500 ppm), Coal (9-6800 ppm), Petrochemical (28-1220 ppm), Pharmaceutical production (0.1-1600 ppm)
Phenol and Phenolic Compounds

## Slide 11
Carcinogenic organic chemical compounds
Formed due to the disinfection of secondary-treated effluents with chloramines, chlorines, and ozone
NDMA (N-nitrosodimethylamine) is one of the most concerning compounds in N-nitrosamine family
Restricted concentration in recycled water to low levels of 0.7 ng/L [4]
N-nitrosamines Compounds

## Slide 12
B. Wastewater Treatment Methods
Physicochemical treatment: coagulation–flocculation process, adsorption, advanced oxidation (i.e. ozone, UV) [highly-graded treatment technology]
Biological treatment: activated sludge and biological trickling filters are used as sewage treatment system
Advanced treatments: ultra-violet (UV) photolysis, ion exchange, membrane bioreactor process and membrane filtration technology such as reverse osmosis (RO) and nanofiltration (NF) treatment methods
Mujtaba and Majozi, 2016:
UK-Egypt-South Africa Workshop on Water Management – WOW 2016, WITS, SA, 5-9 September. http://wow2016.co.za/

## Slide 13
REVERSE OSMOSIS PROCESS
Solvent
Membrane
Feed
Permeate
Particle or Solute Molecule
Spiral-wound RO modules are less susceptible to membrane fouling
Al-Obaidi M.A. and Mujtaba I.M., 2016. Computers and Chemical Engineering, 90, 278–299
Removes undesirable species i.e. salts, pollutants, etc. from seawater, wastewater, etc. by pumping the solution at higher pressure than the osmotic pressure which facilitates solvent flow from the concentrated side to the diluted side

## Slide 14
Fig. 1. Schematic diagram of the spiral-wound module in two dimensions
Spiral-wound module

## Slide 15
a) The Feasibility of the RO Process for Wastewater
Experimental results of Chai et al. [7] showed that the copper rejection is 96.4%
Bódalo-Santoyo et al. [8] confirmed the sulphate rejection between 96 and 99.5%
The ammonium was retained in a lower range of 74 to 84% depends on the membrane type [8]
The rejection of ammonium, cyanide, and sulphate in the range of 92.7-93.5%, 88-90% and 93.8-93.9% [9]
Copper and cadmium removal were 98 and 99% respectively [10]

## Slide 16
a) The Feasibility of the RO Process for Wastewater
Aniline removal between 79% and 91.8% depending on the membrane type [11]
Chromium removal from electroplating industry’s effluents is about 99% [12]
The experiments of Sagne et al. [13] showed that caproic acid and 2.3-butanediol were completely removed and 80% of butyric acid
The experiment of Madaeni and Koocheki [14] showed rejection of 91, 93, 95 and 98-99% for nitrite, nitrate, sulfite and phosphate ions respectively

## Slide 17
b) The RO Process Modelling
A number of models for researching the membrane performance of a spiral wound module with different features and applications based on some assumptions.
The majority of these models did not take into account the impact of operating parameters variation along the membrane dimensions
Distributed models is based on a thorough understanding of the flow pattern inside the module for enhancing the process design

## Slide 18
Distributed Modelling of the Spiral Wound RO Process
Author and year | Assumptions | The Specific Features and advantages | Shortcoming | Field of application
Avlonitis et al. (1991, 1993 and 2007) | Constant physical properties and | Based on the solution-diffusion theory Analytical steady state spatial model | Neglected the diffusive mass transport along the axial and spiral dimensions in both channels | Seawater desalination
Boudinar et al. (1992) | The pressure loss in the two channels being a function of brine and permeate friction parameters (Darcy’s law for porous media) | Based on the solution-diffusion model | Constant fluid density | Seawater desalination
Senthilmurugan et al. (2005) and Mane et al. (2009) | Turbulent flow | Based on the irreversible thermodynamics model Considering the pressure drop in both channels |  | Seawater desalination
Geraldes et al. (2005) | NO pressure drop in the permeate channel | Based on the solution-diffusion model | Neglected the diffusion flow in the feed side | Seawater desalination
Sagne et al. (2009) | Neglected the impact of concentration polarization | Unsteady state one dimensional model based on the solution-diffusion model | Neglected the flux of solute | Seawater desalination
Oh et al. (2009) | Constant mass transfer coefficient | Based on the solution-diffusion model | Constant water flux Ignored the pressure drop in the permeate channel | Seawater desalination
Kaghazchi et al. (2010) |  | Based on the solution-diffusion model | The bulk flow rate was calculated as an average value of inlet and outlet feed flow rates | Seawater desalination
Sundaramoorthy et al. (2011) [15] | Constant values for both the pressure at the permeate channel. | Based on the solution-diffusion model | Constant permeate concentration at the permeate channel | Wastewater treatment
Fujioka et al. (2014) |  | Based on the irreversible thermodynamics model | Zero permeate pressure | Wastewater treatment
Al-Obaidi et al. (2016) [16] | Darcy’s law is valid where the friction parameter was used to characterize the pressure drop in the feed channel | Based on the irreversible thermodynamics model One dimensional model | The average value of permeate concentration was calculated from the inlet and outlet calculated concentrations | Wastewater treatment
Al-Obaidi et al. (2017) [11] | Darcy’s law is valid, the friction parameter used to characterize the pressure drop in the feed channel | Based on the solution-diffusion model Two-dimensional model | The main of the permeate concentration for all the increments has been taken as total fresh water concentration | Wastewater treatment
Table 2. Distributed developed models of spiral wound RO process

## Slide 19: The Comparison between Al-Obaidis’ et al. Developed Models
Al-Obaidi et al. (2016) [16] | Al-Obaidi et al. (2017) [17]
Based on the irreversible thermodynamics model | Based on the solution-diffusion model
One-dimensional model | Two-dimensional model
Isothermal filtration process | The temperature variation is considered
Three transport parameters | Two transport parameters
Table. 3. Comparison between Al-Obaidis’ developed models

## Slide 20
    The Model of Al-Obaidi et al. (2016) [16]
Spiegler and Kedem’s principles were used to elucidate the transport phenomena.
The Darcy’s law is valid where the friction parameter was used to characterize the pressure drop in the feed and permeate channels.
Validity of the film model theory to estimate the concentration polarization impact
Isothermal filtration process
Assumptions

## Slide 21: The Model of Al-Obaidi et al. (2016) [16]
water flux
average bulk concentration
solute flux
feed flow rate
mass transfer coefficient
Governing Equations

## Slide 22: The Model of Al-Obaidi et al. (2016) [16]
bulk pressure
bulk concentration
Permeate flow rate
permeate pressure
and permeate concentrations rejection

## Slide 23: The Model of Al-Obaidi et al. (2016) [16]
The friction and the model transport parameters (b, Lp, Bs, σ) for each run were calculated using the gEST parameter estimation of the gPROMS software based on the experiments conducted by Fujioka et al. [18]
The values used for the friction parameters were 62, 194 and 395 (atm s/m⁴) for the average permeate fluxes 2.78E-6, 5.56E-6 and 8.33E-6 m/s respectively. The selected membrane transport parameters of the three N-nitrosamine solutes (NDMA, NEMA and NPYR) and the water transport parameter Lp are provided in Table 4.
Parameter Estimation

## Slide 24: The Model of Al-Obaidi et al. (2016) [16]
Table 4. Physical and transport parameters of the selected N-nitrosamines
Name | Molecular weight (g/mol) | Permeability coefficient, Bs (m/s) | Water permeability coefficient, (Lp) (m/s atm) at 20 °C | Reflection coefficient, (dimensionless)
NDMA NEMA NPYR | 74.05 88.06 100.06 | 4.75E-6 – 5.36E-6 1.15E-6 – 1.23E-6 4.18E-7 – 4.39E-7 | 1.06E-6 – 1.27E-6 1.05E-6 – 1.21E-6 1.05E-6 – 1.23E-6 | 0.951-0.985 0.936-0.989 0.983-0.998
Name | Molecular weight (g/mol) | Permeability coefficient, Bs (m/s) | Water permeability coefficient, (Lp) (m/s atm) at 20 °C | 
NDMA NEMA NPYR | 74.05 88.06 100.06 | 4.75E-6 – 5.36E-6 1.15E-6 – 1.23E-6 4.18E-7 – 4.39E-7 | 1.06E-6 – 1.27E-6 1.05E-6 – 1.21E-6 1.05E-6 – 1.23E-6 | 0.951-0.985 0.936-0.989 0.983-0.998

## Slide 25
The Model of Al-Obaidi et al. (2016)[16]
Fig. 10 shows that the model is able to simulate the observed data with a minor deviation. In addition, Fig. 11 shows the linear fittings with a regression coefficient R² (close to 1) for the experimental and model prediction of the outlet feed flow rate
Model Validation
Chart: Fb(L) Model (m³/s)
| 2.2300000000000002E-3 | 2.3000000000000008E-3 | 2.3600000000000001E-3
 | 0.0021605 | 0.002267 | 0.002352
Fig. 11. Linear fitting of experimental and model outlet feed flow rate
Fig. 10. Experimental and model rejections of NDMA, NEMA and NDEA with average permeate flux
Chart: Average Permeate Flux, m³/sec
| 8.3299999999999999E-6 | 5.5600000000000001E-6 | 2.7800000000000001E-6
NDMA EXP. | 62.6 | 56.1 | 38.8
NDMA Model | 62.8089 | 54.3438 | 49.4591
NEMA EXP. | 89.402 | 83.424 | 72.826
NEMA Model | 87.1858 | 82.5166 | 70.5266
NPYR EXP. | 95.38 | 94.565 | 89.13
NPYR Model | 94.9343 | 92.5727 | 86.4376

## Slide 26: The Model of Al-Obaidi et al. (2017) [17]
Validity of the solution-diffusion model for the transport of solvent and solute through the membrane
Validity of Darcy's law for the feed channel, which assumes that the pressure drop is proportional to the feed flow rate and the friction parameter is applied to characterize the pressure drop
Validity of the film model theory to estimate the concentration polarization impact
The main value of the permeate concentration for all the increments will be taken as the total fresh water concentration since the flowing of outlet water is in the spiral direction towards the perforated collected pipe
Assumptions

## Slide 27: The Model of Al-Obaidi et al. (2017) [17]
water flux
solute flux
wall membrane concentration
bulk concentration
permeate concentration
mass transfer coefficient
/no. of sub-division average permeate concentration
total permeate flow rate
recovery rate
rejection parameter
Governing Equations

## Slide 28: The Model of Al-Obaidi et al. (2017) [17]
The parameters of the model were estimated using the proposed graphical method of linear fit of Sundaramoorthy et al. [15]. This method was used to determine the values of solvent transport coefficient Aw, solute transport coefficient Bs and the feed channel friction parameter b. The details of these parameters are provided in Table 3.
Parameter Estimation
Table 3. Parameter estimation results
Parameter | Value
Water transport parameter ( | 9.42009E-7
Dimethylphenol transport parameter () | 2.22577E-8
Friction factor ( | 9400.9
Parameter | Value

## Slide 29: The Model of Al-Obaidi et al. (2017) [17]
Fig. 2 shows this for solute rejection for the whole data within 2.1% error.
Model Validation
Chart: Rej(av) (Model)
Fig. 2. Comparison of experimental and model prediction of solute rejection

## Slide 30: The Model of Al-Obaidi et al. (2017) [17]
Fig. 3 shows that the feed flow rate decreases quite quickly as water passes through the membrane
An increase of the concentration polarization and osmotic pressure caused by the build-up of the solute on the membrane causes a reduction in water flux.
Fig. 3. Steady state feed flow rate along the two-dimensions at inlet feed conditions (2.166E-4 m³/s, 6.548E-3 kmol/m³, 13.58 atm and 31.5°C)

## Slide 31: The Model of Al-Obaidi et al. (2017) [17]
Fig. 4 shows that the feed pressure drops at the end of the membrane length due to increasing pressure loss, in turn due to the friction in wall membrane.
Fig. 4. Steady state feed pressure along the two-dimensions at inlet feed conditions (2.166E-4 m³/s, 6.548E-3 kmol/m³, 13.58 atm and 31.5°C

## Slide 32
The model of Al-Obaidi et al. (2017) [17]
Fig. 5. Steady state solute concentration along the two-dimensions at inlet feed conditions (2.166E-4 m³/s, 6.548E-3 kmol/m³, 13.58 atm and 31.5°C)
Fig. 5 clearly shows the spatial progress of feed concentration in two dimensions in the feed channel due to retained solute along the membrane wall

## Slide 33: The Model of Al-Obaidi et al. (2017) [17]
Chart: Inlet Feed Pressure, atm
| 5.83 | 7.7700000000000014 | 9.7100000000000009 | 11.64 | 13.58
8.19E-04 | 0.8823 | 0.9101 | 0.92416 | 0.93347 | 0.94055
1.64E-03 | 0.9016 | 0.9271 | 0.9396 | 0.9478 | 0.9538
2.46E-03 | 0.91 | 0.9345 | 0.9464 | 0.9539 | 0.9595
6.55E-03 | 0.94319 | 0.94545 | 0.95683 | 0.96371 | 0.96854
Fig. 6. Impact of variation in inlet feed pressure and concentration on solute rejection at fixed inlet feed flow rate and temperature (2.583E-4 m³/s and 31oC)
Fig. 6 shows the response of solute rejection for the variation in both inlet feed pressure and inlet feed concentration with constant values of inlet feed flow rate and temperature
Solute rejection increases because of an increase in the inlet feed pressure and concentration

## Slide 34: The Model of Al-Obaidi et al. (2017) [17]
Chart: Inlet Feed Pressure, atm
| 5.83 | 7.7700000000000014 | 9.7100000000000009 | 11.64 | 13.58
2.17E-04 | 0.9244 | 0.946 | 0.9568 | 0.96366 | 0.9685
2.33E-04 | 0.92318 | 0.94588 | 0.95686 | 0.96368 | 0.96855
2.58E-04 | 0.9432 | 0.94549 | 0.9568 | 0.9637 | 0.9685
Fig. 7. Impact of variation in inlet feed pressure and flow rate on solute rejection at fixed inlet feed concentration and temperature (6.548E-3 kmol/ m³ and 31oC)
Fig. 7 depicts the response of solute rejection for the variation in both inlet feed flow rate and inlet feed pressure with constant values of inlet feed concentration and temperature
Increasing inlet feed flow rate has a comparable impact on the solute rejection compared with using low pressures conditions.

## Slide 35: The Model of Al-Obaidi et al. (2017) [17]
Fig. 8 clearly shows the response of solute rejection for the variation in inlet feed concentration and inlet feed flow rate with constant values of inlet feed pressure and temperature
Chart: Inlet Feed Concentration, kmol/m³
| 8.1900000000000028E-4 | 1.6370000000000004E-3 | 2.4550000000000002E-3 | 6.5480000000000017E-3
2.17E-04 | 0.9411 | 0.9543 | 0.9598 | 0.96857
2.33E-04 | 0.94079 | 0.954 | 0.9596 | 0.96855
2.58E-04 | 0.9405 | 0.9538 | 0.9595 | 0.96854
Fig. 8. Impact of variation in inlet feed concentration and flow rate on solute rejection at fixed inlet feed pressure and temperature (13.58 atm and 31oC)

## Slide 36: The Model of Al-Obaidi et al. (2017) [17]
The temperature has a considerable impact on the solute rejection (Fig. 9).
Increasing the operating temperature results in decreasing the viscosity of brine, increasing water flux and reducing the concentration at the permeate channel.
Chart: Inlet Feed Concentration, kmol/m³
| 8.1900000000000028E-4 | 1.6370000000000004E-3 | 2.4550000000000002E-3 | 4.0920000000000002E-3 | 6.5480000000000017E-3
31.5 | 0.92913 | 0.94357 | 0.94976 | 0.95564 | 0.95938
35 | 0.9549 | 0.9631 | 0.96668 | 0.97013 | 0.97234
43 | 0.9795 | 0.98232 | 0.98358 | 0.98483 | 0.98564
Fig. 9. Impact of variation in inlet feed concentration and temperature on solute rejection at fixed inlet feed pressure and flow rate (9.71 atm and 2.166E-4 m³/s)

## Slide 37: C) Conclusions
This research provides a state-of-the-art of distributed models and associated performance of the RO process for the removal of highly toxic organic compounds
The possibilities of the RO process for removing NDMA are yet to be fully explored or realised with many opportunities and challenges for optimising the underlying operating conditions, superstructure and membrane synthesis.
The RO process remains the most promising treatment method for the removal of a wide range of hazardous chemicals albeit dependent on the operating conditions and the process configuration.

## Slide 38: References
[1] Jiménez B.; Asano T.; 2008. Water reuse, an international survey of current practice, issues and needs. London: IWA Publishing.
[2] EFSA, 2013. Scientific opinion on the toxicological evaluation of phenol. EFSA Journal, 11(4), 3189. Available at: http://www.efsa.europa.eu/en/efsajournal/doc/3189.pdf
[3] A.E. Mohammed, A. Jarullah, S. Gheni, I.M. Mujtaba, Optimal design and operation of an industrial three phase reactor for the oxidation of phenol, Comput Chem Eng. 94 (2016) 257-271.
[4] US EPA, 2009. United States Environmental Protection Agency IRIS database. Available at: https://www.epa.gov/iris.
[5] E. Steinle-Darling, M. Zedda, M.H. Plumlee, H.F. Ridgway, M. Reinhard, Evaluating the impacts of membrane type, coating, fouling, chemical properties and water chemistry on reverse osmosis rejection of seven nitrosoalklyamines, including NDMA, Water Res. 41 (2007) 3959-3967.
[6] A. Reverberi, B. Fabiano, C. Cerrato, V. Dovì, Concentration polarization in reverse osmosis membranes: Effect of membrane splitting, Chem. Eng. Trans. 39 (2014) 763-768.
[7] X. Chai, G. Chen, P.-L. Yue, Y. Mi, Pilot scale membrane separation of electroplating waste water by reverse osmosis, J Membr Sci. 123 (1997) 235-242.
[8] A. Bódalo-Santoyo, J.L. Gómez-Carrasco, E. Gómez-Gómez, F. Máximo-Martin, A.M. Hidalgo-Montesinos, Application of reverse osmosis to reduce pollutants presents in industrial wastewater, Desalination, 155 (2003) 101-108.
[9] A. Bódalo-Santoyo, J.L. Gómez-Carrasco, E. Gómez- Gómez, G. León, M. Tejera, Sulfonated polyethersulfone membrane in the desalination of aqueous, Desalination, 168 (2004) 277-282.
[10] H. Abo-Qdais, H. Moussa, Removal of heavy metals from wastewater by membrane processes: a comparative study, Desalination, 164 (2004) 105-110.

## Slide 39: References
[11] J.L. Gómez, G. León, A.M. Hidalgo, M. Gómez, M.D. Murcia, G. Griñán, Application of reverse osmosis to remove aniline from wastewater, Desalination, 245 (2009) 687-693.
[12] H. Mohammadi, M. Cholami, M. Rahimi, Application and optimization in chromium-contaminated wastewater treatment of the reverse osmosis technology, Desalination and Water Treatment, 9 (2009) 229-233.
[13] C. Sagne, C. Fargues, R. Lewandowski, M.-L. Lameloise, M. Gavach, M. Decloux, A pilot scale study of reverse osmosis for the purification of condensate arising from distillery stillage concentration plant, Chemical Engineering and Processing: Process Intensification, 49 (2010) 331-339.
[14] S.S. Madaeni, S. Koocheki, Influence of di-hydrogen phosphate ion performance of polyamide reverse osmosis membrane for nitrate and nitrite removal. J. Porous Mater. 17 (2010) 163-168.
[15] S. Sundaramoorthy, G. Srinivasan, D.V.R. Murthy, An analytical model for spiral wound reverse osmosis membrane modules: part I—model development and parameter estimation, Desalination, 280 (1–3) (2011) 403-411.
[16] M.A. Al-Obaidi, C. Kara-Zaïtri, I.M. Mujtaba, Development and validation of N-nitrosamine rejection mathematical model using a spiral-wound reverse osmosis process, Chem. Eng. Trans. 52 (2016) 1129-1134.
[17] M.A. Al-Obaidi, C. Kara-Zaïtri, I.M. Mujtaba, Wastewater treatment by spiral wound reverse osmosis: Development and validation of a two dimensional process model, J. Cleaner Prod. 140 (2017) 1429-1443.
[18] T. Fujioka, S.J. Khan, J.A. Mcdonald, A. Roux, Y. Poussade, J.E. Drewes, L.D. Nghiem, Modelling the rejection of N-nitrosamines by a spiral-wound reverse osmosis system: Mathematical model development and validation, J Membr Sci. 454 (2014) 212-219.

## Slide 40
Thank you